Silicone Tubing Manufacturing

Making the Silicone

1. Extract out approximately 10 ml of Part A into a syringe. Repeat for Part B
2. Add equal amounts of both Part A and Part B into a plastic cup.
3. Place the plastic cup into the cup holder and then into the mixer.
4. Press “Start” and let the mixer mix for 3 minutes.
5. When done, take out the cup and holder from the mixer and place them into the vacuum. Close the vacuum door.
6. Check that the knob is at “close: and turn the outlet until the outlet is not align with the pin hole.
7. Turn on the AC supply of the pump.
8. Turn knob to “Open”.
9. Start timing for 2 minutes when the minimum pressure is reached.
10. After 2 minutes, turn the knob to “Close”.
11. Turn the outlet to align with the pin hole to let the air out.
12. Open the door with the help of tools if needed.

Making the tube

1. Apply adhesive to the wire.
2. Attach silicone cloth to one side of the wire.
3. Dip the wire into the silicone prepared earlier.
4. Hang the holder in the oven to bake.
5. If the tube is not well done, repeat the dipping and curing process.